## Slide 1: hLRC: Lazy Release Consistency For GPUs
John AlsoP†, Marc Orr‡§, Brad Beckmann§, David Wood ‡§
†UIUC, ‡UW-Madison, §AMD Research

## Slide 2: Motivation
L1
L1
GPU systems use simple coherence actions at synch points
Release synch: flush cache
Acquire synch: invalidate cache
To reduce cost, scoped synchronization is used
Synchronizing threads only flush/inval to the specified scope
L2
t1
t0
wg0
data
t3
t2
wg1
data
acquire
data
release
flush
Scopes complicate memory models, limit sharing patterns

## Slide 3: Motivation
Remote Scope Promotion
Heterogeneous Lazy Release Consistency
 Automatically detect synch locality
 Efficient local synch without scopes
DeNovo Coherence
Lazy Release Consistency
Prior Innovations:
P. Keleher et al. “Lazy release consistency for software distributed shared memory.” in ISCA 1992
M. S. Orr et al. “Synchronization using remote-scope promotion.” in ASPLOS 2015
M. D. Sinclair et al. “Efficient GPU synchronization without scopes: Saying no to complex consistency models.” in MICRO 2015

## Slide 4: Scoped Synchronization
st_rel_agt(L, 0)
st_rel_wg(L, 0)
st_rel_wg(L, 0)
cas_acq_agt(&L, 0, 1)
cas_acq_agt(&L, 0, 1)
Hower et al., ASPLOS 2014
st(data,2)
ld(R1, data)
work-group 0
work-group 1
OK
agent scope
wg_scope0
t1
t0
wg0
wg_scope1
t3
t2
wg1
cas_acq_wg(&L, 0, 1)
ld(R1, data)
thread 0
thread 1
thread 2
flush
OK
Complex memory model - heterogeneous races
Efficient dynamic sharing not possible
SC for HRF = SC for DRF + scopes
L1
L1
L2
RACE!

## Slide 5: Prior Work: Remote Scope Promotion
wg_scopeM
wg_scopeN
Key idea: promote scope at remote cores
  Add new memory orders for remote synch
    Implementation uses broadcasts
  Remote-scope acquire: broadcast flush
  Remote-scope release: broadcast invalidate
Orr et al., ASPLOS 2015
agent scope
wg_scope0
t1
t0
wg0
wg_scope1
t3
t2
wg1
flush
flush
Enables efficient dynamic sharing
Adds complexity to memory model
Implementation does not scale
remote agent scope
flush

## Slide 6: Prior Work: DeNovo coherence
Key idea: Registration reduces flush/invalidation costs
  Obtain exclusive registration for writes and atomics
  L2 keeps track of up-to-date copy (local or remote)
  Release: Register non-registered dirty data
  Acquire: invalidate all non-registered data
Sinclair et al., MICRO 2015
agent scope
wg_scope0
t1
t0
wg0
wg_scope1
t3
t2
wg1
register
R: data
Supports DRF (scope-free) memory model
Exploits locality in registered data
Reuse for non-registered data is limited
Added state, indirection for registration
data

## Slide 7
Remote Scope Promotion
hLRC:
Heterogeneous Lazy Release Consistency
DeNovo Coherence
Lazy Release Consistency

## Slide 8: hLRC: Heterogeneous Lazy Release Consistency For GPUs
Key idea: Exploit synch locality to avoid coherence actions
  Use DeNovo registration for only atomics
  Lazily perform coherence actions only when remote synch detected (LRC for CPUs [ISCA’92])
  Invalidate when cache obtains registration
  Flush when cache loses registration
Our work
agent scope
wg_scope0
t1
t0
wg0
wg_scope1
t3
t2
wg1
flush
Synch locality automatically detected
Minimal added registration overhead
Supports DRF (scope-free) memory model
Sensitive to synchronization locality
atomic
R:atomic
Scopes as software hint

## Slide 9: Comparison Overview
Scopes | Scopes+RSP | DeNovo | hLRC
 Avoid flush/inval for local synch |  Avoid flush/inval for local synch |  Avoid flush/inval for modified data |  Avoid flush/inval for local synch

## Slide 10: Comparison Overview
Scopes | Scopes+RSP | DeNovo | hLRC
 Avoid flush/inval for local synch |  Avoid flush/inval for local synch |  Avoid flush/inval for modified data |  Avoid flush/inval for local synch
 Limited dyn. sharing |  Efficient dyn. sharing |  Efficient dyn. sharing |  Efficient dyn. sharing

## Slide 11: Comparison Overview
Scopes | Scopes+RSP | DeNovo | hLRC
 Avoid flush/inval for local synch |  Avoid flush/inval for local synch |  Avoid flush/inval for modified data |  Avoid flush/inval for local synch
 Limited dyn. sharing |  Efficient dyn. sharing |  Efficient dyn. sharing |  Efficient dyn. sharing
 Hetero races |  Hetero races |  DRF model |  DRF model

## Slide 12: Comparison Overview
Scopes | Scopes+RSP | DeNovo | hLRC
 Avoid flush/inval for local synch |  Avoid flush/inval for local synch |  Avoid flush/inval for modified data |  Avoid flush/inval for local synch
 Limited dyn. sharing |  Efficient dyn. sharing |  Efficient dyn. sharing |  Efficient dyn. sharing
 Hetero races |  Hetero races |  DRF model |  DRF model
 |  Poor scalability |  Data registration overhead |  Sensitive to atomic movement

## Slide 13: Methodology
Simulation environment
Extended version of AMD gem5 APU simulator
128 CUs
16KB L1, 4MB L2
Workloads
Benchmarks from Pannotia benchmark suite [IISWC’13]:
  Single Source Shortest Path (SSSP)
  Graph Coloring (color)
  Pagerank (PR)
Modified to use per-CU task queues and work stealing to address load imbalance
9 graph inputs from Florida sparse matrix collection [TOMS’11]
S. Che et al. “Pannotia: Understanding irregular GPGPU graph applications.” in IISWC 2013
T. Davis et al. “The University of Florida sparse matrix collection.” in TOMS 2011

## Slide 14: Methodology
Scenario | Coherence | Steal enabled? | Pop scope | Steal scope
baseline | Scopes | no | agent | N/A
scope-only | Scopes | no | wg | N/A
steal-only | Scopes | yes | agent | agent
RSP | Scopes+RSP | yes | wg | remote agent
DeNovo-B | DeNovo* | yes | N/A | N/A
hLRC | hLRC | yes | N/A | N/A
*Block-granularity DeNovo is used, with no coherence regions

## Slide 15: Evaluation: Speedup
Chart: Speedup
| SSSP-1 | SSSP-2 | SSSP-3 | color-1 | color-2 | color-3 | PR-1 | PR-2 | PR-3 | geo. mean
baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
scope | 1.1468 | 1.1242 | 1.006 | 1.1047 | 0.9868 | 1.0247 | 1.2345 | 1.0069 | 1.0205 | 1.07
steal | 1.0591 | 1.0017 | 1.2233 | 1.0116 | 1.5222 | 1.0102 | 0.99994 | 1.5518 | 1.173 | 1.1556
RSP | 0.9692 | 1.0456 | 1.0082 | 0.93484 | 1.1787 | 0.75527 | 1.0462 | 1.1464 | 0.66875 | 0.95837
DeNovo-B | 1.1984 | 1.1434 | 1.0347 | 0.87273 | 1.494 | 1.0191 | 1.1937 | 1.6222 | 1.4806 | 1.2061
hLRC | 1.4134 | 1.3748 | 1.2497 | 1.1114 | 1.5683 | 1.0059 | 1.2894 | 1.5422 | 1.1848 | 1.292

## Slide 16: Evaluation: Speedup
Chart: Speedup
| SSSP-1 | SSSP-2 | SSSP-3 | color-1 | color-2 | color-3 | PR-1 | PR-2 | PR-3 | geo. mean
baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
scope | 1.1468 | 1.1242 | 1.006 | 1.1047 | 0.9868 | 1.0247 | 1.2345 | 1.0069 | 1.0205 | 1.07
steal | 1.0591 | 1.0017 | 1.2233 | 1.0116 | 1.5222 | 1.0102 | 0.99994 | 1.5518 | 1.173 | 1.1556
RSP | 0.9692 | 1.0456 | 1.0082 | 0.93484 | 1.1787 | 0.75527 | 1.0462 | 1.1464 | 0.66875 | 0.95837
DeNovo-B | 1.1984 | 1.1434 | 1.0347 | 0.87273 | 1.494 | 1.0191 | 1.1937 | 1.6222 | 1.4806 | 1.2061
hLRC | 1.4134 | 1.3748 | 1.2497 | 1.1114 | 1.5683 | 1.0059 | 1.2894 | 1.5422 | 1.1848 | 1.292
RSP does not scale to 128 cores, degrades performance by up to 33%

## Slide 17: Evaluation: Speedup
Chart: Speedup
| SSSP-1 | SSSP-2 | SSSP-3 | color-1 | color-2 | color-3 | PR-1 | PR-2 | PR-3 | geo. mean
baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
scope | 1.1468 | 1.1242 | 1.006 | 1.1047 | 0.9868 | 1.0247 | 1.2345 | 1.0069 | 1.0205 | 1.07
steal | 1.0591 | 1.0017 | 1.2233 | 1.0116 | 1.5222 | 1.0102 | 0.99994 | 1.5518 | 1.173 | 1.1556
RSP | 0.9692 | 1.0456 | 1.0082 | 0.93484 | 1.1787 | 0.75527 | 1.0462 | 1.1464 | 0.66875 | 0.95837
DeNovo-B | 1.1984 | 1.1434 | 1.0347 | 0.87273 | 1.494 | 1.0191 | 1.1937 | 1.6222 | 1.4806 | 1.2061
hLRC | 1.4134 | 1.3748 | 1.2497 | 1.1114 | 1.5683 | 1.0059 | 1.2894 | 1.5422 | 1.1848 | 1.292
RSP does not scale to 128 cores, degrades performance by up to 33%
DeNovo-B performs best for multiple workloads, but registration overheads limit benefits for others

## Slide 18: Evaluation: Speedup
Chart: Speedup
| SSSP-1 | SSSP-2 | SSSP-3 | color-1 | color-2 | color-3 | PR-1 | PR-2 | PR-3 | geo. mean
baseline | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
scope | 1.1468 | 1.1242 | 1.006 | 1.1047 | 0.9868 | 1.0247 | 1.2345 | 1.0069 | 1.0205 | 1.07
steal | 1.0591 | 1.0017 | 1.2233 | 1.0116 | 1.5222 | 1.0102 | 0.99994 | 1.5518 | 1.173 | 1.1556
RSP | 0.9692 | 1.0456 | 1.0082 | 0.93484 | 1.1787 | 0.75527 | 1.0462 | 1.1464 | 0.66875 | 0.95837
DeNovo-B | 1.1984 | 1.1434 | 1.0347 | 0.87273 | 1.494 | 1.0191 | 1.1937 | 1.6222 | 1.4806 | 1.2061
hLRC | 1.4134 | 1.3748 | 1.2497 | 1.1114 | 1.5683 | 1.0059 | 1.2894 | 1.5422 | 1.1848 | 1.292
RSP does not scale to 128 cores, degrades performance by up to 33%
DeNovo-B performs best for multiple workloads, but registration overheads limit benefits for others
hLRC matches or exceeds the best of scope/steal for all workloads, experiences largest average speedup

## Slide 19: Conclusions
Scopes restrict synchronization efficiency and add complexity
Prior work: RSP
  Embrace scopes: avoid coherence actions for local, implement flexibility via broadcasts
  Memory model more complex, remote scope actions scale poorly
Prior work: DeNovo
  Reject scopes: don’t avoid coherence actions, make them cheaper!
  No hetero races, good registered reuse, limited other reuse, data registration overhead
Our proposal: hLRC
  Avoid coherence actions by automatically detecting synchronization locality
  No heterogeneous races, sensitive to atomic locality - can use scopes as software hints

## Slide 20: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2016 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. SPEC is a registered trademark of the Standard Performance Evaluation Corporation (SPEC). Other names are for informational purposes only and may be trademarks of their respective owners.